## Slide 1: 5. Dynamic Networks
5.1 Historical dynamic networks
5.2 Focused time-delay neural network
5.3 Distributed time-delay neural network
5.4 Layer recurrent network
5.5 NARX network
5.6 Computational power of dynamic networks
5.7 Learning algorithms
5.8 System identification
5.9 Model reference adaptive control
5.10 MATLAB Live Script examples

## Slide 2: Introduction
Time
  An essential ingredient of the learning process
  Important for many practical tasks: speech, vision, signal processing, control
Many applications require temporal processing
  Time series prediction
  Noise cancelation
  Adaptive control
  System identification
  ...
  Linear systems  well-developed theories
  Nonlinear systems  neural networks have the potential to solve such problems

## Slide 3: Introduction
How can we build time into the operation of neural networks?
  Extending static neural networks into dynamic neural networks  networks become responsive to the temporal structure of input signals
  Networks become dynamic by adding
  TEMPORAL MEMORY and/or FEEDBACK
Feedback loop

## Slide 4: Static vs. dynamic networks
Neural network categories
Static networks  structural pattern recognition
  Feedforward networks
  No feedback elements, no delays
  Output is calculated directly from the input through feedforward connections
Dynamic networks  temporal pattern recognition
  Output depends on
    current input to the network
    also on previous inputs
    previous network output
    previous network states
  Dynamic networks can be divided into two categories
    Networks that have only feedforward connections
    Networks with feedback or recurrent connections
A need for short-term memory and feedback

## Slide 5: Memory
Memory
  Long-term memory
    Acquired through supervised learning and stored into synaptic weights
  Short-term memory
    Temporal memory, useful to capture temporal dimension
    Implemented as time delays at various parts of the network
Long-term memory

## Slide 6: Tapped delay line
The simplest form of short-term memory
  Already mentioned in linear adaptive filters
  Most commonly used for dynamic networks
  Tapped delay line (TDL) consists of N unit delay operators
  Output of TDL is an N+1 dimensional vector, composed of current and past inputs

## Slide 7: 5.1 Historical dynamic networks
Hopfield (1982)
Jordan (1986)
Elman (1990)
Notes: Images: Ben Krose, Patrick van der Smagt (1996) An Introduction to Neural Networks

## Slide 8: Hopfield network
Hopfield network (Hopfield, 1982)
  Network consists of N interconnected neurons which update their activation values asynchronously and independently of other neurons
  All neurons are both input and output neurons
  Activation values are binary (-1, +1)
  Multiple-loop feedback system  interesting to study the stability of the system
  Primary applications
    Associative memory
    Solving optimization problems

## Slide 9: Jordan network
Jordan network (Jordan, 1986)
  Network outputs are fed back as extra inputs (state units)
  Each state unit is fed with one network output
  The connections from output to state units are fixed (+1)
  Learning takes place only in the connections between the input to hidden units as well as hidden to output units
  Standard backpropagation learning rule can be applied to train the network

## Slide 10: Elman network
context units
Elman network (Elman, 1990)
  Similar to the Jordan network, with the following differences:
  Hidden units are fed back (instead of output units)
  Context units have no self-connections

## Slide 11: 5.2 Focused time-delay neural network
The most straightforward dynamic network  feedforward network + tapped delay line at input
  Temporal dynamics only at the input layer of a static network
  Nonlinear extension of linear adaptive filters
  Backpropagation training can be used
  The structure is suitable for time-series prediction

## Slide 12: MATLAB Live Script example
NN5b_NAR_network.mlx
  Design a nonlinear autoregressive (NAR) neural network for the recursive prediction of chaotic Mackay-Glass time series.
Objective
  Design Focused time-delay neural network for recursive one-step-ahead predictor
  Fixed network parameters
    Number of hidden layers = 1
    Hidden layer activation functions = Logistic
    Output layer activation function = Linear
  Variable network parameters
    Input delays = ?
    Hidden layer neurons = ?
Notes: This is an introduction to the example NN5b_NAR_network.mlx
Mackay-Glass time series represents a nonlinear (chaotic) dynamic system.
We wish to construct a predictor for recursive one-step-ahead prediction.
Some network parameters are chosen as fixed, and others are open to experimentation (variable network parameters).

## Slide 13: Understanding input delays
Input delays = [0 6 12]  Inputs {x(t), x(t-6), x(t-12)}
Prediction horizon = 1  Output x(t+1)
Input delays = [0 6 12]
Prediction horizon = 1
Known world
Unknown world
Notes: The slide graphically presents the meaning of choosing input delays for the neural network predictor.

## Slide 14: Results with 8 hidden neurons and different input delays
(A)
(B)
Notes: Results for different configurations are shown. The upper graph shows a less successful solution, and the lower graph shows a very good solution with accurate multi-step ahead predictions.

## Slide 15: 5.3 Distributed time-delay neural network
Tapped delay lines distributed throughout the network
  Distributed temporal dynamics  ability to handle non-stationary environments
  Backpropagation training cannot be used anymore  the need for temporal backpropagation
  Possible applications:  phoneme recognition, recognition of various frequency contents in signals

## Slide 16: Temporal backpropagation
Backpropagation algorithm
  Suitable for static networks and focused time-delay neural networks
Temporal backpropagation
  Supervised learning algorithm
  Extension of backpropagation
  Required for distributed time-delay neural networks
  Computationally demanding
Which form of backpropagation to use?
  Based on the nature of the temporal processing task
  STATIONARY ENVIRONMENT  Standard backpropagation + Focused time-delay neural networks
  NON-STATIONARY ENVIRONMENT  Temporal backpropagation + Distributed time-delay neural networks

## Slide 17: Example (1/2)
Wan (1994): Time series prediction by using a connectionist network with internal delay lines
  Winner of the “Santa Fe Institute Time-Series Competition”, USA (1992)
  Task: Nonlinear prediction of a nonstationary time series exhibiting chaotic pulsations of NH3 laser

## Slide 18: Example (2/2)
Prediction results

## Slide 19: 5.4 Layer recurrent network
Layer recurrent network = Recurrent multilayer perceptron
  One or more hidden layers
  Each computation layer has a feedback link
Notes: Images: Simon Haykin (2009) Neural Networks and Learning Machines, 3rd ed. (p. 795-796)

## Slide 20: Layer recurrent network structure
Feedback loop with a single delay for hidden layer
  Can be trained by backpropagation
Elman (1990)

## Slide 21: Example (1/3)
Phoneme detection problem
  Recognition of various frequency components
Layer recurrent network
  1 hidden layer
  8 neurons
  5 delays

## Slide 22: Example (2/3)
Network training
  Successful recognition of two “phonemes”

## Slide 23: Example (3/3)
Network testing
  Unreliable generalization, works only on trained phonemes
OK
OK

## Slide 24: 5.5 NARX network
Networks discussed so far
  Focused or distributed time delays
  Feedback only localized to specific network layers
NARX = Nonlinear AutoRegressive Network with EXogenous Inputs
  Recurrent network with global feedback
  Feedback over several layers of the network
  Based on the linear ARX model
  Defining equation for the NARX model
    Output y is a nonlinear function of past outputs and past inputs
    Nonlinear function f can be implemented by a neural network

## Slide 25: NARX structure
NARX network with global feedback
Possible application areas
    Nonlinear prediction and modeling
    Adaptive equalization of communication channels
    Speech processing
    Automobile engine diagnostics

## Slide 26: NARX training considerations
  NARX output is an estimate of the output of some nonlinear dynamic system
  Output is fed back to the input of the feedforward neural network  parallel architecture
  True output is available during training  possible to create series-parallel architecture
    True output is used instead of feeding back the estimated output
  Advantages of series-parallel architecture for training
    Training input to the feedforward network is more accurate  improved training accuracy
    The resulting network is purely feedforward  static backpropagation can be used

## Slide 27: MATLAB demo
Maglev Modeling
  This example illustrates how a NARX neural network can model a magnet levitation dynamical system.
  A) Open-loop training configuration B) Closed-loop configuration for recursive prediction
Notes: Please refer to Maglev Modeling, https://uk.mathworks.com/help/deeplearning/ug/maglev-modeling.html

## Slide 28: 5.6 Computational power of dynamic networks
Fully and partially connected recurrent networks

## Slide 29: Theorems
Theorem I (Siegelmann & Sontag, 1991)
  All Turing machines* may be simulated by fully connected recurrent networks built on neurons with sigmoid activation functions. *Turing machine is a theoretical abstraction that is functionally as powerful as any computer
Theorem II (Siegelmann et. al. 1997)
  NARX networks with one layer of hidden neurons with BOSS* activation functions and a linear output neuron can simulate fully connected recurrent networks with BOSS* activation functions, except for a linear slowdown *BOSS = bounded, one-sided saturated function
Corollary to Theorem I and II
  NARX networks with one hidden layer of neurons with BOSS* activation functions and a linear output neuron are Turing equivalent.

## Slide 30: 5.7 Learning algorithms
Two modes of training for recurrent networks
Epochwise training
  For a given epoch, the recurrent network starts running from some initial state until it reaches a new state, at which point the training is stopped and the network is reset to the initial state for the next epoch
  METHOD: Backpropagation through time
Continuous training
  Suitable if no reset states are available or online learning is required
  Network learns while it is performing
  The learning process never stops
  METHOD: Real-time recurrent learning

## Slide 31: Backpropagation through time
Extension of the standard backpropagation algorithm
  Derived by unfolding the temporal operation of the network into a layered feedforward network
  The topology grows by one layer at every time step
  EXAMPLE: unfolding the temporal operation of a 2-neuron recurrent network

## Slide 32: Backpropagation through time example (1/2)
Nguyen & Widrow (1989): The truck backer-upper
Notes: https://doi.org/10.1109/IJCNN.1989.118723

## Slide 33: ... example (2/2)
Training
Generalization

## Slide 34: 5.8 System Identification
System identification = experimental approach to modeling the process with unknown parameters
  STEP 1: Experimental planning
  STEP 2: Selection of a model structure
  STEP 3: Parameter estimation
  STEP 4: Model validation
Unknown nonlinear dynamical process  dynamic neural networks can be used as an identification model
  Two basic identification approaches:
  System identification using a state-space model
  System identification using an input-output model
Notes: Chapters "5.8 System Identification" and "5.9 Model-reference adaptive control" present examples of applications of dynamic networks.

## Slide 35: System identification using a state-space model
“State”
  A vital role in the mathematical formulation of a dynamical system
  State of a dynamical system is defined as a “set of quantities that summarizes all the information about the past behavior of the system that is needed to uniquely describe its future behavior, except for the purely external effects arising from the applied input.”
Plant description by a state-space model
  State:
  Output:
  f, h: unknown nonlinear vector functions
  Two dynamic neural networks can be used to approximate f and h

## Slide 36: State-space solution to the identification problem
  Both networks are trained by gradient descent  minimizing error signals eI and eII
Neural network (II)
  Identification of plant output
  Actual state x(n) is used as input rather than the predicted output
Neural network (I)
  Identification of plant state
  State must be physically accessible!
Notes: Images: Simon Haykin (1999) Neural Networks: A Comprehensive Foundation, 2nd ed. (p. 799)

## Slide 37: System identification using an input-output model
If the system state is not accessible  identification by input-output model
Plant description by an input-output model
  f is unknown nonlinear vector function
  Input-output formulation is equivalent to NARX formulation
  NARX neural network can be used to approximate f
  q past inputs and outputs should be available

## Slide 38: Input-output solution to the identification problem
  NARX neural network can be used as a dynamic identification model
  Series-parallel learning
    system output is used as feedback, not the predicted output
  Parallel architecture for application

## Slide 39: 5.9 Model-reference adaptive control
Dynamic networks are important for feedback control systems
  MULTIPLE PROBLEMS:
  Nonlinear coupling of plant state with control signals
  Presence of unmeasured or random disturbances
  Possibility of a nonunique plant inverse
  Presence of unobservable plant states
MRAC = Model reference adaptive control
  Well suited for the use of neural networks
  Possible control methods:
    Direct MRAC
    Indirect MRAC
Notes: Chapters "5.8 System Identification" and "5.9 Model-reference adaptive control" present examples of applications of dynamic networks.

## Slide 40: MRAC using direct control
Unknown plant dynamics  adaptive learning
Controller + plant = closed-loop feedback system
  Controller and plant build externally recurrent network
  How to get plant gradients  indirect control
Notes: Images: Simon Haykin (1999) Neural Networks: A Comprehensive Foundation, 2nd ed.

## Slide 41: MRAC using indirect control
Two-step procedure to training the controller
  Identification of the plant (identification model)
  Using the plant model to obtain dynamic derivatives to train the controller
  Controller and plant model build externally recurrent network
Notes: Images: Simon Haykin (1999) Neural Networks: A Comprehensive Foundation, 2nd ed. (p. 803)

## Slide 42: Summary
  Layer recurrent network
Focused time-delay neural network
  Distributed time-delay neural network
  NARX network

## Slide 43: 5.10 MATLAB Live Script examples
NN5b_NAR_network.mlx
  Design a nonlinear autoregressive (NAR) neural network for the recursive prediction of chaotic Mackay-Glass time series.